BeamProfiler_pd1

# Install heat sinks one the Pi
0.	https://raspberrytips.com/install-heat-sinks-raspberry-pi/
# Setting up your Raspberry Pi
https://projects.raspberrypi.org/en/projects/raspberry-pi-setting-up
1.	insert SD-card
2.	connect the mouse to a USB-port
3.	connect a keyboard to a USB-port
4.	connect a screen via HDMI
5.	connect power supply to micro-USB	(the Pi starts to boot)

# Finish Setup
6.	select corresponding settings

# Install python3 with corresponding libraries on the Pi
7.	(https://tutorials-raspberrypi.de/opencv-auf-dem-raspberry-pi-installieren/)
https://www.alatortsev.com/2018/09/05/installing-opencv-3-4-3-on-raspberry-pi-3-b/
OR:
sudo apt install python3-opencv

Access via ssh:
https://www.raspberrypi.org/documentation/remote-access/ssh/

8.	install matplotlib
sudo pip3 install matplotlib
9.	if numpy must be updated
sudo pip3 install –upgrade numpy
10.	install PIL.ImageTk
sudo apt-get install python3-pil.imagetk
11.	follow installation instruction for camera-library: https://github.com/basler/pypylon
11.1	download pylon-software for OperatingSystem: ARM-32-bit
https://github.com/Basler/pypylon/releases: install corresponding lib :
for python 3.5 install pypylon-1.3.1-cp35-cp35m-linux_armv7l.whl
pip3 install pypylon-1.3.1-cp35-cp35m-linux_armv7l.whl

11.2 To commit permission for executing the shell script by double click go to desktop and type:
chmod u+x BeamProfiler.sh
# Connect Pi with Touchscreen
12. Remove screws of controller board at the backside of the display, put Pi on the appropriate screw socket and mount the Pi with the screws
13. connect the cables from the controller board with the Pi as shown in the following link:
https://maker-tutorials.com/raspberry-pi-touchscreen-installieren-und-anschliessen-tipps-tricks/
14. start the Pi and if necessary rotate the display with the following command:
„sudo nano /boot/config.txt“
and add the following line on the top of the file:
„lcd_rotate=2“
15. save the file and test the shell script „BeamProfiler.sh“ on the Desktop